## Slide 1
Network Part 1
Network Fundamentals • LAN/WLAN/PAN/MAN/WAN • Internet • Topologies

## Slide 2
2. What Is a Network?
A computer network is a collection of connected devices that can communicate and exchange data using agreed rules called protocols.
The devices do not all have to be computers. The important idea is that they have a way to exchange information.
Computer A ←────────→ Computer B

## Slide 3
3. What Can Be Connected to a Network?
Networks can contain many kinds of devices.
Examples include computers, servers, phones, printers, cameras, switches, routers, firewalls, wireless access points, virtual machines, and IoT devices.
Depending on context, connected devices may be called hosts or nodes.

## Slide 4
4. Why Do We Build Networks?
Networks allow systems to communicate and share resources instead of operating as isolated devices.
A network can support file sharing, printers, applications, databases, authentication, email, Internet access, and security monitoring.

## Slide 5
5. A Network Does Not Require the Internet
Two or more devices can communicate across a local network without having Internet access.
If an Internet connection fails, local services may still work. Computers may still reach local printers, servers, domain controllers, and other devices.
PC-A ───── Switch ───── PC-B
No Internet required

## Slide 6
6. Network Communication Needs Rules
Connecting devices is only part of networking. Devices also need agreed rules that define how communication works.
These rules are called protocols.
Examples you will study later include Ethernet, IP, ARP, TCP, UDP, DNS, DHCP, and HTTP.

## Slide 7
7. Wired Networks
A wired network uses physical cabling to carry network signals.
Copper Ethernet commonly uses electrical signaling. Fiber-optic networking uses light.
Wired networks are common in offices, server rooms, data centers, and home networks.
PC ─── Ethernet cable ─── Switch

## Slide 8
8. Wireless Networks
Wireless networks allow devices to communicate without a network cable attached to the device.
Wi-Fi uses radio signals. A wireless access point provides wireless devices with access to the network.
Laptop ))) Wireless Access Point ─── Network

## Slide 9
9. LAN — Local Area Network
LAN stands for Local Area Network.
A LAN connects devices within a relatively limited environment such as a home, office, school, building, or lab.
LAN describes the scope of the network, not whether it has Internet access.

## Slide 10
10. LAN Example
A small office might have computers, a server, and a printer connected through local networking equipment.
Those devices can communicate locally and share resources as part of the LAN.
PC-A ──┐
PC-B ──┼── Switch ─── Server
Printer─┘

## Slide 11
11. WLAN — Wireless Local Area Network
WLAN stands for Wireless Local Area Network.
It is a local-area network in which wireless technology such as Wi-Fi provides network access.
A WLAN is still a local network; wireless describes how devices connect to it.

## Slide 12
12. Wireless Access Point
A wireless access point, or AP, allows wireless devices to connect into a network.
At home, one device may combine several functions such as wireless access, switching, routing, DHCP, NAT, and firewalling. Those functions are separate concepts even when they are inside one box.
Phone )))
Laptop ))) → Access Point → Network

## Slide 13
13. PAN — Personal Area Network
PAN stands for Personal Area Network.
A PAN covers a very small range centered around a person and their devices.
Bluetooth connections between a phone, headphones, keyboard, mouse, or similar personal devices are common examples.
Phone ← Bluetooth → Headphones

## Slide 14
14. MAN — Metropolitan Area Network
MAN stands for Metropolitan Area Network.
It describes networking across an area larger than a typical LAN but smaller than the geographic scope normally associated with a WAN.
A MAN may connect buildings or sites across a city or metropolitan region.

## Slide 15
15. WAN — Wide Area Network
WAN stands for Wide Area Network.
A WAN provides connectivity across larger geographic distances and can connect separate LANs.
Organizations may use WAN connectivity to link offices, branches, data centers, or other distant locations.

## Slide 16
16. LAN and WAN Together
A company can have a LAN at each location while using WAN connectivity between those locations.
The local networks remain distinct, but the WAN provides a way for them to communicate across distance.
Toronto LAN → WAN → Vancouver LAN

## Slide 17
17. What Is the Internet?
The Internet is a massive global system of interconnected networks.
Your computer is not directly connected to every server in the world. Traffic can move through your local network, service provider networks, and other networks before reaching its destination.
Your PC → LAN → Router → ISP → Other Networks → Destination

## Slide 18
18. Network Topology
Network topology describes how devices and connections in a network are arranged.
Topology helps us describe network structure. Common examples include star, bus, ring, and mesh topologies.

## Slide 19
19. Star, Bus, and Ring Topologies
Star topology: devices connect through a central device, commonly a switch in modern Ethernet LANs.
Bus topology: devices share a common communication medium.
Ring topology: devices are arranged in a ring-like structure.
STAR: PCs → Switch ← Server
BUS: A ─── B ─── C ─── D
RING: A → B → C → D → A

## Slide 20
20. Mesh + Physical vs Logical Topology
Mesh topology provides multiple interconnections between nodes. A full mesh connects every node directly to every other node; a partial mesh provides multiple paths without every possible direct link.
Physical topology describes how equipment is physically connected. Logical topology describes how communication is logically organized or how traffic flows.
Devices can share physical infrastructure while belonging to different logical networks.
Physical = how equipment is connected
Logical = how communication is organized

## Slide 21
21. Host vs Node
A node is any device or connection point that participates in a network.
A host is generally an endpoint that has a network address and can send or receive network communication.
Computers and servers are common examples of hosts. The word node is broader and can also describe networking devices depending on context.
The exact terminology can vary, so always pay attention to how the term is being used.

## Slide 22
22. What Is a Network Interface?
A network interface is the connection point through which an operating system sends and receives network traffic.
A computer can have more than one interface. Examples include Ethernet, Wi-Fi, loopback, and virtual interfaces.
Because IP addresses are assigned to interfaces, one computer can have multiple IP addresses when it has multiple interfaces.
Computer
├── Ethernet interface
├── Wi-Fi interface
└── Loopback interface

## Slide 23
23. NIC vs Network Interface
NIC stands for Network Interface Card or Network Interface Controller.
The NIC or network adapter provides network connectivity. The operating system exposes a network interface that software can use.
A physical Ethernet adapter can provide an Ethernet interface, while virtual machines can use virtual network adapters and interfaces.
Not every interface requires a physical NIC. Loopback is an important example.

## Slide 24
24. Network Media
The network medium is the path through which communication signals travel.
Copper cabling commonly carries electrical signals. Fiber-optic cabling carries light. Wireless networking uses radio waves.
Different media have different characteristics, including distance, capacity, interference resistance, and installation requirements.
Copper → Electrical signals
Fiber → Light
Wi-Fi → Radio waves

## Slide 25
25. What Is a Protocol?
A protocol is a defined set of rules that systems follow when communicating.
Protocols specify things such as how information is structured, interpreted, transmitted, and responded to.
Networking works because communicating systems follow compatible rules.
Later lessons will study protocols such as Ethernet, IP, ARP, TCP, UDP, DNS, DHCP, and HTTP.

## Slide 26
26. Network Infrastructure Devices
Infrastructure devices help build, connect, control, or protect networks.
A switch helps connect devices on Ethernet LANs. A router connects IP networks. A firewall controls traffic according to security rules. A wireless access point provides wireless network access.
These are only high-level definitions. Each device will be studied separately later.
PCs / Servers → Switch → Router / Firewall → Other Networks
↑
Wireless Access Point

## Slide 27
27. Endpoints vs Infrastructure Devices
An endpoint is typically a device that uses or provides network services, such as a workstation, server, phone, printer, or camera.
Infrastructure devices support the network itself, such as switches, routers, firewalls, and wireless access points.
The distinction is useful when reading diagrams and troubleshooting because endpoints and infrastructure devices perform different roles.

## Slide 28
28. Intranet vs Internet
An intranet is a private internal network or collection of internal resources intended for members of an organization.
The Internet is the global system of interconnected networks.
An organization can operate internal websites, applications, file servers, and other resources on its intranet while also providing users with access to the Internet.
Internal PC → Company Intranet
↘
Internet

## Slide 29
29. Reading a Basic Network Diagram
Network diagrams visually represent devices and the connections between them.
Read a simple diagram by identifying the endpoints first, then the infrastructure devices, then the links between them.
A line usually represents some form of connection. The exact meaning depends on the diagram, so labels and context matter.
Later, diagrams can also show IP networks, interfaces, VLANs, routes, firewalls, and other logical information.
PC → Switch → Router → Internet
↑
Server

## Slide 30
30. Network Part 1 Recap
A network allows connected devices to communicate and exchange data using protocols.
LAN, WLAN, PAN, MAN, and WAN describe different networking scopes or forms of connectivity. The Internet is a global network of interconnected networks.
Networks can use copper, fiber, or wireless media. Their arrangement can be described using topologies such as star, bus, ring, and mesh.
Hosts and endpoints use network services, while infrastructure devices help connect, control, and protect the network.
This foundation prepares us for the next topic: MAC addresses.