## Slide 1
Network Part 3
Data • Bits & Bytes • Packets • Frames • Encapsulation • Network Performance

## Slide 2
2. What Actually Travels Across a Network?
When we say one computer sends a file, webpage, message, or security event to another computer, the object is represented as digital data.
Networking systems organize and process that data so it can travel across network links and be understood by the receiving system.
The complete file is not physically moved as one solid object.

## Slide 3
3. What Is Data?
Data is information represented in a form a computer can process.
Text, images, audio, video, files, application messages, and security logs are all forms of data.
At the lowest digital level, this information can be represented using binary values.
Data → binary representation → transmission

## Slide 4
4. What Is a Bit?
A bit is a binary digit.
A bit has two possible values: 0 or 1.
Bits are the basic units used to represent digital information. Network speeds are also commonly expressed in bits per second.
0 or 1

## Slide 5
5. What Is a Byte?
A byte is a group of eight bits.
Bytes are commonly used when describing data sizes, while network transmission rates are commonly expressed in bits per second.
Keeping bits and bytes separate prevents many networking calculations from becoming confusing.
8 bits = 1 byte

## Slide 6
6. Bits vs Bytes
A lowercase b commonly represents bits, while an uppercase B commonly represents bytes.
For example, Mbps means megabits per second, while MB can mean megabytes.
Because one byte contains eight bits, 100 MB and 100 Mb are not the same amount of data.
b = bit
B = byte
8 bits = 1 byte

## Slide 7
7. Why Data Is Handled in Smaller Units
Large amounts of application data are not normally treated as one enormous indivisible network transmission.
Networking protocols process information in smaller structured units.
This allows systems and networking devices to handle, forward, verify, and manage communication efficiently.

## Slide 8
8. Protocol Data Units
As data moves through networking functions, different layers use different names for the structured information they handle.
Terms you will commonly encounter include segment, datagram, packet, frame, and bits.
We are introducing the vocabulary here. TCP, UDP, and the OSI/TCP-IP models will explain the terminology more precisely later.

## Slide 9
9. What Is a Packet?
A packet is a structured unit of data associated with the network layer.
In our IPv4 studies, the important example is an IP packet.
An IP packet carries information needed for IP communication along with the payload being transported.
IP Packet = IP Header + Payload

## Slide 10
10. Basic Information in an IP Packet
An IPv4 packet contains an IP header and payload.
The header includes fields used to process the packet. Important examples include the source IP address and destination IP address.
The payload contains information supplied by an upper-layer protocol.
Source IP → 192.168.1.10
Destination IP → 192.168.1.20

## Slide 11
11. What Is a Header?
A header is protocol control information placed before the data that a protocol is carrying.
Headers tell networking systems how to interpret and process communication.
Different protocols have different headers because they solve different problems.
HEADER + PAYLOAD

## Slide 12
12. Header vs Payload
The header contains information used by the protocol.
The payload is the data being carried by that protocol.
A payload can itself contain another protocol's header and data. This nesting is a key reason encapsulation is so important.
[ Header ][ Payload ]

## Slide 13
13. What Is a Frame?
A frame is a data-link-layer unit.
On an Ethernet network, an Ethernet frame can carry an IP packet.
A frame and a packet are therefore related, but they are not interchangeable terms.
Ethernet Frame
└── IP Packet

## Slide 14
14. Packet vs Frame
An IP packet contains network-layer information such as source and destination IP addresses.
An Ethernet frame contains data-link information used for delivery over the Ethernet link.
The packet can be carried inside the frame.
Later, MAC addresses will make the Ethernet frame much easier to understand.
FRAME
└── PACKET
└── Upper-layer data

## Slide 15
15. What Is Encapsulation?
Encapsulation is the process of adding protocol information around data as it moves through the networking stack.
Each networking function adds the information it needs.
The result is similar to placing one structured message inside another structured container.
Application Data
↓
Transport information
↓
IP Packet
↓
Ethernet Frame

## Slide 16
16. Encapsulation — Simplified Example
An application produces data.
A transport protocol can add transport information. IP can then add an IP header. Ethernet can place the resulting packet inside a frame.
The exact names depend on the protocols involved, but the central idea is that information is wrapped as it moves downward.
Frame → Packet → Transport Data → Application Data

## Slide 17
17. What Is Decapsulation?
Decapsulation is the corresponding process at the receiving system.
The receiving networking stack processes the relevant protocol information and passes the remaining payload upward toward the appropriate application.
Encapsulation prepares data for transmission; decapsulation processes it at the destination.

## Slide 18
18. Sending and Receiving — Big Picture
The sending application creates data. Networking protocols prepare it for transmission. The network interface transmits the information across a medium.
The receiving interface accepts the communication. Networking protocols process it, and the appropriate application ultimately receives the data.
Application → Network Stack → Medium → Network Stack → Application

## Slide 19
19. Physical Transmission
Eventually, information must cross a physical or wireless medium.
The digital information is represented through signaling appropriate to that medium.
Networking therefore connects logical information such as packets and frames with real physical transmission.
Digital data → signals → medium → signals → digital data

## Slide 20
20. Copper, Fiber, and Wireless Signals
Copper networking commonly represents information using electrical signaling.
Fiber-optic networking uses light.
Wi-Fi uses radio-frequency electromagnetic waves.
These technologies carry network information differently even though higher-level networking concepts can remain similar.
Copper → electrical
Fiber → optical
Wi-Fi → radio

## Slide 21
21. What Is Bandwidth?
Bandwidth describes the capacity of a network link to carry data.
It is commonly expressed in bits per second.
Common examples include 100 Mbps, 1 Gbps, and 10 Gbps.
Higher bandwidth means greater data-carrying capacity; it does not automatically mean lower delay.
100 Mbps 1 Gbps 10 Gbps

## Slide 22
22. Bandwidth Is Capacity
A useful analogy is the width of a road.
A wider road can accommodate more traffic at once. Similarly, a higher-bandwidth link can carry more data per unit of time.
The analogy is not perfect, but it helps separate capacity from latency.

## Slide 23
23. What Is Latency?
Latency is the delay involved in communication from one point to another.
It is commonly measured in milliseconds.
Lower latency generally means less delay. Applications such as voice, gaming, and interactive remote sessions can be especially sensitive to latency.
5 ms < 50 ms < 150 ms

## Slide 24
24. Bandwidth vs Latency
Bandwidth and latency describe different properties.
Bandwidth is capacity. Latency is delay.
A connection can have high bandwidth and still have noticeable latency. A lower-bandwidth connection can sometimes have low latency.
Do not use the word speed as a substitute for both concepts.
Bandwidth = capacity
Latency = delay

## Slide 25
25. What Is Throughput?
Throughput is the actual rate of data transfer achieved over a period of time.
A link may have a nominal capacity of 1 Gbps while a particular transfer achieves less than 1 Gbps.
Protocol overhead, congestion, device limitations, wireless conditions, and other factors can affect observed throughput.
Link capacity: 1 Gbps
Observed throughput: 700 Mbps

## Slide 26
26. Bandwidth vs Throughput
Bandwidth describes the capacity available on a link.
Throughput describes the rate actually achieved during communication.
The two numbers may be different.
This distinction is important when troubleshooting a user who says, 'I pay for 1 Gbps but my transfer is slower.'
Bandwidth ≠ guaranteed throughput

## Slide 27
27. What Is Packet Loss?
Packet loss occurs when packets do not successfully reach their intended destination.
Loss can result from congestion, faulty links, interference, overloaded equipment, intentional filtering, or other network conditions.
Different protocols and applications respond to packet loss differently.
Packet 1 → ✓
Packet 2 → ✓
Packet 3 → X
Packet 4 → ✓

## Slide 28
28. What Is Jitter?
Jitter is variation in packet delay over time.
For example, packets may arrive after 20 ms, then 22 ms, then 80 ms, then 19 ms.
Even when average latency appears acceptable, large variations can affect real-time applications such as voice and video.
20 ms → 22 ms → 80 ms → 19 ms

## Slide 29
29. Network Performance Is More Than 'Speed'
Network performance can involve several different measurements.
Bandwidth describes capacity. Latency describes delay. Throughput describes actual transfer rate. Packet loss describes missing packets. Jitter describes variation in delay.
Understanding which measurement is unhealthy leads to better troubleshooting.
Bandwidth | Latency | Throughput | Loss | Jitter

## Slide 30
30. Network Part 3 Recap
Network communication begins with data represented digitally using bits and bytes.
Protocols organize information using headers and payloads. IP uses packets, while Ethernet uses frames. Encapsulation wraps data with protocol information, and decapsulation processes it at the receiving system.
Physical media carry the resulting information using electrical, optical, or radio signaling.
Bandwidth, latency, throughput, packet loss, and jitter describe different aspects of network performance.
With the network foundation complete, the next isolated topic is MAC addresses.